#### List of Topics

Internal registers 		1

Memory Map			2

Signals EPP-1.9			3

Epp ports for programmers	4

Modes				5

Cycles				6

EXCHANGE N64 <> PC		7

Epp Time Diagramm		8

Block diagramm			9

- Internal registers

| # |  | mode | Bits | name | Descriptions |
| --- | --- | --- | --- | --- | --- |
| 0 | RG0 | R w | D[7..0] | a[7..0] | Support count address |
| 1 | RG1 | R w | D[7..0] | a[15..8] | Only 0 bit support count address |
| 2 | RG2 | R w | D[7..0] | a[23..16] |  |
| 3 | RG3 | w | D[2..0] | a[26..24] |  |
| 3 | RG3 | R | D3 | Don’t use |  |
|  |  |  | D4 | Pc | 1 = pc can work with DRAMM |
|  |  |  | D5 | Wcf | wcf 1 = was write cart b4000000-b7FFFFFF |
|  |  |  | D6 | Wdf | 1 = was write dramm |
|  |  |  | D7 | Rst | 1 = power on n64 |
| 4 | RG4 | R w | D[7..0] | Data | Read and write dramm |
|  | RG5 | w | D0 | Pc | 1 - enable PC mode, DRAMM connect to PC |
|  |  |  | D1 | Cart_on | 0 - cart ROM off from n64 1 - cart ROM on |
|  |  |  | D2 | Write_en | 0 – DRAMM read only 1 – DRAMM write enable |
|  |  |  | D[4..3] | Don’t use |  |
|  |  |  | D5 | Wcfset | 0 – clear wcf, 1 – set wcf |
|  |  |  | D6 | Wdfset | 0 – clear wdf, 1 – set wdf |
|  |  |  | D7 | Don’t use |  |

- Memory Map

| Mode | pc | Cart_on | Wcf | B0000000-B3FFFFFF | b4000000-b7FFFFFF |
| --- | --- | --- | --- | --- | --- |
| PC | 1 | 0 | 0 | Nothing | Nothing |
| PC | 1 | 0 | 1 | Cart | Cart |
| PC | 1 | 1 | 0 | Nothing | Cart |
| PC | 1 | 1 | 1 | Cart | Cart |
| N64 | 0 | 0 | 0 | Dramm | Dramm |
| N64 | 0 | 0 | 1 | Cart | Cart |
| N64 | 0 | 1 | 0 | Dramm | Cart |
| N64 | 0 | 1 | 1 | Cart | Cart |

N.B.        Wcf seting to 1 if you wrote to B4XXXXXX area and CART_ON = 1

- Signals EPP-1.9

PV-backup use standart EPP-1.9 protocol and epp_init is only reset of device.

| Epp_write | 0 – write cycle 1 – read cycle |
| --- | --- |
| Epp_addr_stb | 0 – write addres |
| Epp_data_stb | 0 – write data |
| Epp_init | 0 – rest |
| Epp_busy | 0 – ready 1-wait |
| Epp_data[7..0] | Datas of EPP |

- Epp ports for programmers

Base:=$378	{base addres of EPP}

const rga = 3 ; rgd = 4; rgc = 2; rgs = 1;

rg_addr:=base + rga 	{address register }

rg_data:=base + rgd 	{data register}

rg_cntr:=base + rgc	{control register}

rg_stat:=base + rgs	{status register}

# In_reg (number of register) data

Rg_addr:=number of register

Result:=rg_data

# Out_reg (number of register, data)

Rg_addr:=number of register

Rg_data:=data

# Set_reg (number of register)

Rg_addr:=number of register

# In_sec ()data

Result:=rg_data

# Out_sec (data)

Rg_data:=data

Out_cntr (data)

Rg_cntr:=data

Out_stat (data)

Rg_stat:=data

- Modes

PV-backup can work in 3 diference modes.

- Game playing from cartrige

- Game playing from dramm

- Game playing from dramm but cartrige on

- Debug mode, in this mode n64 can read and write dramm, read cartrige and exchange information with PC.

- Cycles

# Const

Mwrite_on = 4

Mcart_on = 2

Mpc = 1

Msetwcf = $20

# Reset

Rg_cntr:=0

…

delay timeout

…

rg_cntr:=4

## Pc_mode 		{DEBUG MODE write on, cart on}

Rg_stat:=1

Out_reg(rg5, mwrite_on + mcart_on +1 )

# N64mode

Rg_stat:=1

Out_reg(rg5, mwrite_on + mcart_on)

## Pc_mode 		{DRAM PLAY MODE}

Rg_stat:=1

Out_reg(rg5, 1 )

# N64mode

Rg_stat:=1

Out_reg(rg5, 0)

## Pc_mode 		{CART PLAY MODE cart on, wcf =1 }

Rg_stat:=1

Out_reg(rg5, msetwcf + mcart_on +1 )

# N64mode

Rg_stat:=1

Out_reg(rg5, msetwcf + mcart_on)

## Pc_mode 		{DRAM AND CART PLAY MODE  cart on}

Rg_stat:=1

Out_reg(rg5,  mcart_on +1 )

# N64mode

Rg_stat:=1

Out_reg(rg5, mcart_on)

# Set_pointer

Out_reg(0,addres[7..0])

Out_reg(1,addres[15..8])

Out_reg(2,addres[23..16])

Out_reg(3,addres[26..24])

# Read_pointer

Addres:=in_reg(0) + in_reg(1) * $100 + in_reg(2) * $10000 + in_reg(3) * $1000000

# Write_datas

Set_pointer

Set_reg(rg4)

Begin  of loop

Out_sec(data)

End_loop

# Read_datas

Set_pointer

Set_reg(rg4)

Begin  of loop

Data:=in_sec

End_loop

# Read_status

Status:=in_reg(rg3)

- EXCHANGE N64 <> PC

| PC do | N64 do |
| --- | --- |
| Write data to dramm |  |
| Set n64 debug mode |  |
| Delay | N64 found dramm and work |
| ……. | ….. ….. |
| While wcf = 0 do {wait for wcf} |  |
|  | IN TO BREAK POINT |
|  | Read Write data to dramm |
|  | Write to b4XXXXXX |
| Set pc debug mode | While (b0XXXXXX is ROM) do {see N.B.} |
| Read write dramm |  |
| Set n64 debug mode |  |
| Goto line 3 | Dramm found |
|  | Read dramm |
|  | EXIT TO BREAK POINT |

N.B. Checking of presents dramm in the b0XXXXXX area can be:

You can select for you word in cartrige who<> 0 and <>FFFF

For examle word b4FFFFFF = 55AA

You write inverse data to B3FFFFFF

($B3FFFFFF):=$AA55

And now, you can alltimes check dramm for busy (ROM)

IF ($B3FFFFFF)<>$AA55 THEN DRAMM is busy

- Epp Time Diagramm

EPP_SS IS

| S0 | S1,SA,S0 | S1,SD,S0 | S1,SD,S0 | S1,SA,S0 | S1,SR,SR1,S0 | S1,SR,SR1,S0 |
| --- | --- | --- | --- | --- | --- | --- |
|  | Wr addr | Wr data | Wr data | Wr addr | Wr dramm | Rd dramm |

- BLOCK DIAGRAMM

EOF (